## Slide 1: Modeling and Validation of Reflecting Metasurfaces for Improved mmWave Coverage
Padmashree Reddy
Supervisor: Simon Häger
11.10.2023
Master Thesis Interim Presentation

## Slide 2: Outline
Motivation
Methodology and Implementation
Results and Conclusion
Timeline and Next Steps

## Slide 3: Potential of mmWave Communication
Buildings with metasurface
BS
Advantages:
Higher bandwidth and data rates
Network capacity extension
Disadvantages:
Higher path loss
Susceptibility to blockage
Beam management
Communication link with metasurfaces
 | Transmitted/received power
 | Transmitter/receiver gain
 | Path loss from Tx-IRS and IRS-Rx.
 | Gain at the Metasurface
 | Transmitted/received power
 | Transmitter/receiver gain
 | Path loss from Tx-IRS and IRS-Rx.
 | Gain at the Metasurface
Typical communication link
P1
P2
P3
LOS
NLOS
VLOS
Metasurfaces deployment in mmWave Communication

## Slide 4: Deployment of Passive and Active Metasurfaces
M
Reflected wave
Transmitted wave
Advantages:
Enhanced signal coverage and quality
Flexibility and adaptability
Disadvantages:
Synchronization and coordination
Complexity and cost
Building with metasurface
Array of active elements
Reflected wave
Control board
Copper plate
Transmitted wave
: Element size
M, N : Array size
: Slope angle
: Beam orientation
Need to optimize the deployment of HELIOS reflectors and improve performance gain.
Intelligent Reflecting Surfaces
HELIOS Reflectors
Additional Advantages:
Low power consumption
Easy integration and cost-effective
Disadvantages:
Limited control
Lack of reflection pattern adaptation in real-time
Array of passive elements
Motivates network planning!

## Slide 5: Existing Model Extension
Models | Modified Power Received Formula | Gain at the Reflector
Rx
Tx
[1] Ö. Özdogan, E. Björnson and E. G. Larsson, "Intelligent Reflecting Surfaces: Physics, Propagation, and Pathloss Modeling," in IEEE Wireless Communications Letters, vol. 9, no. 5, May 2020.
[2] K. Ntontin et al., "Optimal Reconfigurable Intelligent Surface Placement in Millimeter-Wave Communications," European Conference on Antennas and Propagation (EuCAP), March 2021.
[3] W. Tang et al., "Wireless Communications With RIS: Path Loss Modeling and Experimental Measurement," in IEEE Transactions on Wireless Communications, vol. 20, no. 1, Jan. 2021
[1] |  | 
[1] |  | 
[2] |  | 
[2] |  | 
[3] |  | 
[3] |  | 
Similarities
Differences

## Slide 6: Comparison of IRS Models
0
Maximum gain when Tx/Rx orthogonal to the reflector surface.
Loss of gain when reflector focuses away from surface normal.
User is at angle where reflector is pointing at i.e., .
Angle sweep along user, supports radiation patterns i.e.,
variation [deg]
IRSgain [dB]
IRSgain [dB]

## Slide 7: Conceptualizing Reflection Model for HELIOS

## Slide 8: 2. HELIOS Module Concept [4]
b
Reflecting
surface
Reflected wave
Transmitted wave
Simulation Analysis when
Slope angle variation
Reflector length variation
Material conductivity variation with copper
[4] S. Häger, K. Heimann, S. Böcker and C. Wietfeld, "Holistic Enlightening of Blackspots With Passive Tailorable Reflecting Surfaces for Efficient Urban mmWave Networks," in IEEE Access, vol. 11, 2023..
Reflector
Surface
Normal
Incident wave
()
Wall
surface
normal
X
Y
Z
RCS Analytical Model for flat plate )
: Element size
M, N : Array size
: Slope angle
: Beam orientation
RCS Analytical Model for HELIOS )
(Previous)
(Begun)
(Aim)

## Slide 9: Simulated Results from HELIOS Module
Similar to IRS model [1-3]
Saturation as the main lobes is out-of-range of the considered far field
Validating
when =
Gain (dB)
Gain (dB) linear scale
Reflector length (cm)
Slope angle (deg)
Copper conductivity values (Siemens/m)
Where exponent n=1.05
Similar to IRS model [1-3]

## Slide 10: 2. Analytical Modeling of HELIOS element: Bistatic Radar-Cross-Section (RCS)
[5] C.A. Balanis, Advanced Engineering Electromagnetics. Ed. 2, Chapter 11, John Wiley & Sons, 2012.
[6] D. E. Kerr, Propagation of Slwrt Radio Waves, hl.1.T. Rad. Lab. Ser.,So. 13. Lexington, Mass.: Boston Tech. Pub., 1964.
[7] S. Häger, K. Heimann, S. Böcker, C. Wietfeld, "Holistic Enlightening of Blackspots with Passive Tailorable Reflecting Surfaces for Efficient Urban mmWave Networks," In IEEE Access, vol. 11.
)
Aspects | Basic equation for flat plate | Modified equation for HELIOS )
Aspects |  | 
Reflector Size |  | 
Reflector Size |  | 
Supported angles |  | 
Supported angles |  | 
Rotation of reflecting surface |  | 
Rotation of reflecting surface |  | 
Beamwidth correction factor |  | 1/2
Basic equation for flat plate
Modified equation for HELIOS
[5-7]

## Slide 11: 3. Comparison of Analytical and Simulated values: Variation of Width
Behavior when
Behavior when
Crossover when which is part of both the curves.
Gain increases with reflector size.
They both behave the same!

## Slide 12: 3. Comparison plot of HELIOS Reflector Module
10
Simulated and analytical model match as desired!
Gain matches.
1st side lobe Matches.
2nd side lobe matches.
= =
Beams get narrower as reflector size increases.

## Slide 13: 3. Heatmap Comparison of Analytical and Simulations: HELIOS Reflector Element
Theta [deg]
Gain [dB]
Analytical Model
Simulations
Phi [deg]
Side lobes match
There are sufficient similarities between both.
This variation is a work in progress.

## Slide 14: 3. Comparison of Analytical and Simulated values: Reflector Array [8]
1xN array
MxN array
1.22 dB
0.44 dB
No self-shadowing
RCS doesn’t account for self-shadowing yet.
[8] M. I. Skolnik, "Radar Handbook," 3rd ed., New York, NY, USA: McGraw-Hill, 2008.
Shadowed
region
Transmitted wave
Reflected wave

## Slide 15: 3. Heatmap Comparison of Varied Analytical and Simulated Values:
Beams get narrower with higher gains.
Lot of similarities can be observed.
But
2x2 HELIOS
4x4 HELIOS
8x8 HELIOS
Phi [deg]
Gain [dB]
Side lobe beamwidth matches
RCS model doesn’t account for diffractions, as the model is kept simple.
Analytical Model
Simulations
Theta [deg]
0 10 20 30
0 10 20 30
0 10 20 30
30
25
20
15
10
5
0
30
25
20
15
10
5
0

## Slide 16: 3. HELIOS Extension for Broader Beams
Changes by delta
Changes by
+𝑑𝑒𝑙𝑡𝑎/𝑛°
+𝑑𝑒𝑙𝑡𝑎/𝑛°
+𝑑𝑒𝑙𝑡𝑎/𝑛°
+𝑑𝑒𝑙𝑡𝑎/𝑛°
+𝑑𝑒𝑙𝑡𝑎/𝑛°
+𝑑𝑒𝑙𝑡𝑎/𝑛°
Reflection is broadened.
Long simulations using HFSS
Desired reflection can be achieved faster
RCS Analytical Model for HELIOS )
Reflection is narrow.
Beams get broader.

## Slide 17: 4. Timeline
Stage 1
Literature reading
Stage 2
Stage 3
Implementation, Reinterpretation of IRS models
Stage 4
Familiarization with a thesis template
Preparation of kickoff presentation
HELIOS simulation with Ansys HFSS
HELIOS array simulation and modeling
Working on thesis section 3
Preparation of the second presentation
Optimizing and evaluating HELIOS model according to design requirement
Working on thesis section 4
Preparation of the third presentation
Working on the thesis’s final section
Preparation of the final presentation
Radar Cross Section (RCS) for planar surface
Comparing analytical and Ansys simulation
Tuning of analytical model

## Slide 18: 4. Next Steps: Addressing Self-Shadowing
X
Y
Z
Shadowed Region
Where is shadowing factor
Optimized analytical model
Transmitted wave
Reflected wave
of the reflecting surface will be shadowed
Modified equation for HELIOS module

## Slide 19: 4. Next Steps: Assessing Impact in Specific Scenarios
Overall communication link:
UMi: Urban Micro
UMa: Urban Macro
FSPL: Free Space Path Loss
LOS: FSPL, 3GPP UMi and UMa scenarios
Transmitter
)
Receiver Grid
)
Reflectors
)
NLOS
VLOS
IRS Models
Notes: 𝜃_𝑇𝑥 ", (" 𝜃_𝑅𝑥−2⋅𝛾"), " 𝜑_𝑇𝑥 ", " 𝜑_𝑅𝑥

## Slide 20: Thank you!